## Slide 1
General-Purpose Code Acceleration with Limited-Precision Analog Computation
ISCA 2014
Georgia Institute of Technology The University of Texas at Austin University of Washington Microsoft Research
Renée St. Amant Amir Yazdanbakhsh Jongse Park Bradley Thwaites Hadi Esmaeilzadeh Arjang Hassibi Luis Ceze Doug Burger
Georgia Institute of Technology Alternative Computing Technologies (ACT) Lab
Notes: Thanks Boris for the introduction. Today, I am going to talk about how to accelerate general-purpose code with limited-precision analog computation which has been historically a tough challenge. This work is a collaboration between GaTech, UTAustin, UW, and Microsoft research.

## Slide 2
Input and Output
Display
Communication
Sensing
Processing
Storage
Analog Domain
Digital Domain
Analog Accelerator
Notes: Modern system on a chips are a collection of various analog and digital components.
Analog components are mostly placed on the IO side and used for data sensing, communication, and display.
And, Digital components are used for data processing and storage. One of the most important part of the digital processing is programmable accelerators such as GPU and FPGA.
**** CLICK ****
In this work, we push the accelerators from the digital domain to the analog domain to use the inherent efficiency of the analog circuits.

## Slide 3
How to use analog circuits for accelerating programs written in conventional languages?
1) Neural transformation [Esmaeilzadeh et. al., MICRO 2012]
2) Analog neurons
3) Compiler-circuit co-design
Notes: But the main research question that we are trying to answer is “How to use analog circuits to accelerate diverse set of programs written in conventional languages? ”
Today if you stay with me, I will show you how to do this.
Throughout the presentation, we are going to stick with three design principles which are:
First, Neural Transformation. We use neural transformation to transform regions of code to a common neural representation.
Second, Analog neurons. We push the design of neuron itself into the analog domain while keeping the rest of the accelerator design in the digital domain.
Third, Compiler-circuit co-design. We account for analog design limitations by exposing those limitations up to the compiler stack.
During my talk, I am going through each of these three design principles and describe why and how we use each of them in our analog accelerator.

## Slide 4: Challenges
- Analog circuits are mainly single function
- Instruction control cannot be analog
- Storing intermediate results in analog domain is not effective
- Analog circuits have limited operational range
1) Neural transformation
2) Analog neurons
3) Compiler-circuit co-design
Notes: There are many challenges in performing analog acceleration.
First of all, analog circuits are mainly single function and Instruction control cannot be implemented in the analog domain.
To tackle these, we use our first design principle which is neural transformation.

## Slide 5: Challenges
- Analog circuits are mainly single function
- Instruction control cannot be analog
- Storing intermediate results in analog is not effective
- Analog circuits have limited operational range
1) Neural transformation
2) Analog neurons
3) Compiler-circuit co-design
Notes: Storing intermediate results with current analog CMOS technology is not effective.
This is where our second design principle comes into play. We only push the design of neuron itself into the analog domain and use digital circuit for buffering and storing any intermediate results.

## Slide 6: Challenges
- Analog circuits are mainly single function
- Instruction control cannot be analog
- Storing intermediate results in analog domain is not effective
- Analog circuits have limited operational range
1) Neural transformation
2) Analog neurons
3) Compiler-circuit co-design
Notes: Next challenge is that analog circuits have limited operational range.
We address this by our third design principle which is compiler-circuit co-design. Exposing analog limitations up to the compiler stack enables us to diminish the negative effects of those limitations.
Having said that, let’s move on to our first design principle which is….
****** CLICK *******

## Slide 7
1st Design Principle
Neural Transformation

## Slide 8: Neural Transformation
Analog Neural Network
Analog Neural Network
Esmaeilzadeh, Sampson, Ceze, Burger, “Neural Acceleration for General-Purpose Approximate Programs,” MICRO 2012.
Notes: The way that neural transformation works is that we ask the programmer to write the program in any conventional programming languages and delineate region of the code as approximable. Which means if I introduce a little bit of error in this region it is not going to be the end of the world.
Whatever I am going to talk about from now on, is automatically done in the compiler. What I am gonna do is to put probes on the inputs and outputs of the marked region. Then I compile this code and run the binary with bunch of test cases provided by the programmer. Then I collect the inputs and outputs to this region of the code. And then we use these training data to train a neural network.
After this neural network reaches a certain level of accuracy, I am going to replace that region with a neural network which could be analog.

## Slide 9: A-NPU acceleration
Neural Representation
Code1
Code2
Code3
Code4
Code5
Code6
…
CPU
A-NPU
Source Codes
Common Intermediate Representation
Acceleration
+
×
Chart: 
Notes: The good thing about the neural algorithmic transformation is it converts different regions of code from various applications to a neural representation.
This neural representation provides us generality in the sense that we can transform different applications to a common intermediate representation that only includes simple operations which are addition, multiplication and a simple sigmoid function.
Unlike the original complicated instructions in the code, these simple operations can be effectively implemented in the analog domain.
This enables us to accelerate diverse set of applications with analog circuits, but we should bear in mind that the analog accelerator needs to be reconfigurable. Because different codes are transformed to neural networks with different topologies.
So, after talking about our first design principle which was neural transformation, let’s move to our second design principle which is … ***** CLICK *****

## Slide 10
2nd Design Principle
Analog Neurons
Notes: ANALOG NEURONS

## Slide 11: Analog Neurons for Accelerated Computation
V to I
V to I
V to I
Notes: On the left side you see a conceptual view of a neuron. Let’s see how it works. We take bunch of inputs and then we multiply each of these inputs to their corresponding constant weight. And then we sum up the result of the multiplications and pass this summation through a nonlinearity function which is a sigmoid.
Let’s see how we can implement this conceptual neuron in the analog domain.On the right side you can see the high-level design abstraction of an analog neuron.
We take the digital inputs and use D-to-As to convert them to current levels which correspond to the input values. And then we pass these current values through variable resistances whose values correspond to the value of the weights. Now what we have is the voltage values which equals to the multiplication of the inputs and their corresponding weights. Then we convert the voltages to currents and simply tie the wires together and use the Kirchoffs law to very efficiently perform the summation.
Finally, when we are converting the result to the digital domain. We use a special A-to-D that actually implements the nonlinearity function by using the physical properties of the transistors which is the saturation property.
This design not only provides a very simple and very efficient implementation of each neurons, but also provide a fair amount of computation to amortize the cost of Digital to analog and analog to digital conversions.
****** CLICK ********
** again raise the limitation **
It seems too nice and dandy. Does it mean that it is all what we need? Did we solve all the problems? Of course not!
Let’s take a step back and look more closely at the basic limitations that we have in analog circuits. I mentioned that we want to encode information with the current and voltage levels, but can we represent arbitrary number of bits with current and voltage levels? The answer is no, one of the most prevalent limitations in analog design is the bounded range of voltages and currents within which the circuits can operate effectively. For example, the voltage margin that we have in this technology node is from 0 to 0.9. We can not represent arbitrary number of bits with this limited range. The larger amount of information that we cram into this bounded range, the more susceptible our design will be to noise and variability and in addition to this practical ADC can not handle very fine granular quantization levels. So we need to carefully put enough margin around each current and voltage level to reduce this susceptibility and make the design practical.
Do you think that’s enough? Let’s look at our design again. We are multiplying inputs to their corresponding weights and then sum them up. We can not afford arbitrary number of inputs to this neuron unit with the bounded range of voltage and current that we have in our hand. Therefore, we need to carefully engineer the number of inputs to each neuron. Increasing the number of ANU inputs translates to encoding a larger value range in a bounded voltage and current range which is impractical. So here there is a tradeoff and interesting design decision which has to delicately be made. The larger the number of inputs and add that can be done in parallel in the analog domain, increasing efficiency. However, due to the limited range of voltage and current that we have, increasing the number of inputs requires decreasing the number of bits per inputs and weights. Through, circuit-level simulations, we empirically found that limiting the number of inputs to 8 with 8-bit inputs and weights strike a good balance between accuracy and efficiency. We don’t have such a restriction in the digital NPUs and we basically can have arbitrary topologies of neural networks. However, this unique ANU limitations restrict the topology of the neural network that can run on the analog accelerators.
The last but not the least, the saturation behavior of sigmoid function in the analog domain is not as smooth as digital implementation.
Having all of these limitations, we should ask ourselves that “how can we address them?” We have a solution for that. Exposing these limitations to the compiler stack and having a customized training algorithm which account for circuit non-idealities can alleviate those limitations. Let’s see how our proposed compilation framework work.

## Slide 12: Mixed-signal A-NPU
Notes: We use these analog neurons to build a RECONFIGURABLE mixed signal neural processing unit.
This A-NPU can execute different topologies of neural networks that are statically scheduled on the analog neurons.
I should emphasize that re-configurability is a key factor here because different applications require different neural networks.
I would like to remind you to our second design principle. Analog Neurons. Here you can see that we only push the neuron itself into the analog domain and all the scheduling, buffering and storage are performed in the digital domain.

## Slide 13
Notes: We actually have a detailed design for each neuron. We had the noise susceptibility of analog circuits in mind when we were designing this circuit.
This is why that we use differential implementation that makes the design more robust to the noise.
I refer you to the paper for the details of the design.

## Slide 14: Limitations of Analog Neuron
Limited range of operation (e.g. 600mV)
Margins for noise resiliency (2-3 mV)
Limited Bit-width
Topology Restriction
Circuit Non-idealities (e.g., Sigmoid)
Notes: This sounds all nice and dandy but there are still two fundamental limitations in the analog domain.
First , the analog circuits only behave linearly in a limited range of voltage or current.
And second, When encoding values, we need to provide enough margin between different quantization levels to make the design noise resilient.
These limitations introduce three challenges to our design.
First, limited bit-width. The input and weight bit-width will be limited. We can not have 32-bit values encoded in the analog domain.
Second, We can not have an arbitrary number of inputs to each neuron which restrict the topology of the neural networks.
And finally, there will be circuit non-idealities. For example, the sigmoid that we can get from the analog circuit is not as ideal and smooth as the digital one.
So we introduce our third design principle to address all of these limitations. Let’s move on to the third design principle which is….. ***** CLICK *****

## Slide 15
3rd Design Principle
Compiler-Circuit Co-design

## Slide 16: Digital Compilation Workflow
Notes: But let’s first look at the original digital compilation workflow.
After the programmer has annotated the source code with approximable regions. The compiler trains a neural network and produces the config file for the neural accelerator and instrumented binary code which allows the core to invoke the the digital NPU. Since we don’t have any specific limitations in the digital domain for implementing neurons, we don’t need to consider any feedback loop from the digital npu to the compiler.
But that doesn’t work for the analog circuit.

## Slide 17: Analog Compilation Workflow
Notes: In the analog circuit, wee need to consider and expose the limitations of the analog npu, which are limited bit-width, topology restrictions and circuit non-idealities, up to the compiler stack and design a customized training algorithm to take into account all these limitations when training the neural network for the analog npu. And that’s exactly what we did in our work.
I am gonna touch some aspects of the customized training algorithm

## Slide 18: (1) Training with Limited Bit-width
Back propagate the error through the fully-precise neural network
Calculate the output error from the limited-precision neural network
Input the training data to the discretized neural network
Train a fully-precise neural network
Limited-Precision Network
Fully-Precise Network
Continuous-Discrete Learning Method (CDLM), E. Fiesler, 1990
Notes: So how the customized training algorithm works?
We use Continuous-Discrete Learning Method to train a neural network with limited bit-width.
The algorithm considers two neural networks. One which is fully precise and the other one which has limited precision.
In the initial phase, CDLM first trains a fully-precise network with a standard training algorithm such as backpropagation. Then, it discretize the input, weight, and the output values according to the exposed analog specification.
The algorithm calculates the new error from the limited-precision network and backpropagates that error through the fully-precise network and updates the weight values accordingly. The process repeats for a limited iterations to get the final discretized weight values.

## Slide 19: (2) Training with topology restrictions and non-idealities
1) Robust to the topology restrictions
2) Tolerate a more shallow sigmoid activation steepness over all applications
Resilient Back Propagation (RPROP), M. Riedmiller, 1993
Notes: CDLM deals with the limited bit width and we used resilient backpropagation which is a variant of backpropagation to deal with the topology restrictions and the non-ideal sigmoid.
Our empirical data shows that RPROP is robust to the topology restrictions and can deal with the non-ideal sigmoid, which is shallower, in the analog domain. I refer you to the paper for the details of the algorithm.

## Slide 20: Measurements Signal Processing, Robotics, 3D Gaming, Financial Analysis, Compression, Machine Learning, Image Processing
Analog A-NPU with 8 Analog Neurons
Transistor-Level HSPICE Simulation
Digital Components
Power Models: McPAT, CACTI, and Verilog
Processor Simulator
Marssx86 Cycle-Accurate Simulation
Predictive Technology Models (PTM), 45nm
Intel Nehalem-like 4-wide/5-issue OoO processor
Technology: 45 nm, Vdd: 0.9 V, f: 3.4 GHz
Vdd: 1.2 V, f: 1.1 GHz
Notes: We evaluated our technique with a diverse set of applications from signal processing to financial analysis, allllllllllll
For the analog part we implemented the design in the transistor-level and performed the Hspice simulation.
We limit the input and weight bit-width to 8-bit and have maximum 8 inputs to each neuron. Our data shows that this design decision strikes a good balance between efficiency and accuracy.
The analog neuron processing unit is clocked three times slower than the core itself. This margin provides enough time to perform computation in the analog domain.

## Slide 21: Speedup
24.5
Chart: Application Speedup
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
Digital NPU | 14.1 | 1.1 | 7.9 | 2.3 | 1.5 | 0.5 | 2.4 | 2.5
Analog NPU | 10.4 | 0.2 | 3 | 3.9 | 0.3 | 0.3 | 0.7 | 1.2
Ranges from 0.8× to 24.5× with Analog NPU
1.2× increase in application speedup with Analog over Digital NPU
2.5
3.7
14.1
10.9
Analog NPU
8-bit Digital NPU
Notes: Here y-axis shows the whole application speedup. The blue bar indicates the speedup with 8-bit digital npu and the green bar shows the increase in the speedup by using analog npu.
Analog NPU provides 3.7x speedup compared to 8-bit digital NPU which provides only 2.5x speedup. This is because the amount of parallelism with the analog NPU is much more than the digital one.
ANPU can perform 64 multiply-adds in parallel, while the digital npu can only performs eight. Therefore, the more complicated neural network that we have, the more speedup we get from the analog npu.
****** ONLY IF THERE IS 15:00 TIME *******
In one application, Kmeans, we see slowdown. The reason is that the transformed region of code in Kmeans consists of 26 mostly arithmetic instructions that can efficiently run on the core. While the neural network for this benchmark is comparatively complex and involves more computation than the original code.

## Slide 22: Energy Savings
Chart: Application Energy Reduction
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
Digital NPU | 42.5 | 1.6 | 25.8 | 7.3 | 2.2 | 1.1 | 2.7 | 5.1
Analog NPU | 8.7 | 0.1 | 4.2 | 10.5 | 0.1 | 0.2 | 0.1 | 1.2
Energy saving with Analog NPU is very close to ideal case (6.5x)
5.1
6.3
42.5
51.2
25.8
30.0
17.8
Analog NPU
8-bit Digital NPU
Notes: Here y-axis shows the application energy reduction. Again the blue bar shows the 8-bit digital NPU while the green bar indicates the increase in the energy savings with analog npu. On average we see 1.2x increase in the energy saving by using analog circuits.
This result is due the fact that the energy cost of executing instructions in the von Neumann, out-of-order pipeline is much more higher than performing simple multiply-adds in the analog domain.
***** CLICK *****
We also compared the energy savings with the ideal case which means zero energy consumption for the offloaded work. The dashed bar shows the maximum energy savings that we can get out of the accelerator. You can see that the analog npu pushes the energy savings very close to the ideal case. And this is because of the efficient design of the analog npu and using only basic laws of physics for the computation

## Slide 23: Application quality loss
Chart: Application-Level Error
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
D-NPU | 0.0602 | 0.0275 | 0.062 | 0.1768 | 0.0548 | 0.0321 | 0.0389 | 0.053422
A-NPU | 0.0418 | 0.0135 | 0.032 | 0.0202 | 0.0292 | 0.0409 | 0.0131 | 0.028467
Quality loss is below 10% in all cases but one
Based on application-specific quality metric
2.8%
Analog NPU
8-bit Digital NPU
Notes: And finally here on y-axis we can see the application-level error for both digital NPU and analog NPU.
The blue bar represents the application error with digital NPU and the red bar shows the increase in the error when we use the analog NPU.
All the errors are measured based on the application-specific quality metric.
In all, but one application we see error less than 10% in both digital and analog domain.
On average, analog NPU introduces 2.8 percent more error than using the digital circuit to the application which is pretty good.

## Slide 24
3%
46%
Speedup
Energy Reduction
What is left?
We can not reduce the energy of the computation much more.
Notes: The current mixed-signal design performs well enough that only 3% and 46% additional improvements in application-level energy consumption and performance are possible with improved accelerator designs.
The speedup is close to ideal case and the only limiting factor here is Amdahl’s law. Due to the high parallelism of the analog npu, we can get a significant speedup by executing conventional codes with limited parallelism on the ANPU.
Implementing multiply, add and sigmoid operations with analog circuits makes our design very close to the ideal case. So there is little value in designing more sophisticated A-NPU.

## Slide 25
Kirchhoff's Law
Ohm’s Law
Saturation Property of Transistors
3.7x × 6.3x ≈23x
Speedup
Energy Reduction
Quality Degradation: Avg. 8.2%, Max. 19.7%
Energy-Delay Product
Notes: I hope that I have shown you that not only it is feasible but also it is significantly efficient to use analog circuits and the basic laws of physics such as Kirchhoff’s law, Ohm’s law, and saturation property of transistors, to run conventional code.
I think the 23X improvement in the energy-delay product with a quality degradation of 8.2 percent on average provides a fair bargain to move toward analog accelerators.

## Slide 26
1) Broad applicability of the analog computation
2) Prototyping and integrating A-NPU within noisy high performance processors
3) Reasoning about the acceptable level of error at the programming level
It is still the beginning...
Notes: But this is still the beginning!
First, Even though we have examined a diverse set of applications, we still need to investigate the broad applicability of the analog computation.
Second, We also need to investigate the feasibility of integrating the analog NPU within the noisy environment of a digital high performance processor through prototyping
And last but not the least. Right now the 10% quality degradation is the magic number for the approximate computing. It is an interesting research path to study how the end-user might reason about the acceptable level of error when an application undergoes an approximate execution.
We believe that the significant gains of using analog circuits to accelerate code provides a very encouraging path forward.
By that, I would be more than happy to take your questions.

## Slide 27
Backup Slides

## Slide 28: Area Breakdown
Sub-circuit | Area
A-NPU | 
8x8-bit DAC | 3,096 T
8xResistor Ladder (8-bit weights) | 4,096 T + 1 K ( 450 T)
8xDifferential Pair | 48 T
I-to-V Resistors | 20 K ( 30 T)
Differential Amplifier | 244 T
8-bit ADC | 2,550 T + 1K ( 450)
Total | 10,964 T
6.6x fewer transistors in the analog neuron implementation
D-NPU | 
8x8-bit multiply-adds | 56,000 T
8-bit Sigmoid lookup table | 16,456 T
Total | 72,456

## Slide 29: Power Breakdown
Sub-circuit | Percentage of total power
A-NPU | 
SRAM-accesses | 13%
DAC-Resistor Ladder-Diff Pair-Sum | 54%
Sigmoid-ADC | 33%
Power numbers vary with applications

## Slide 30: Applications
Signal Processing fft
34 x86 instructions
67.4% dynamic instructions
1➙4➙4➙2
Error: 4.1%
Robotics inversek2j
100 x86 instructions
95.9% dynamic instructions
2➙8➙2
Error: 9.4%
3D Gaming jmeint
1,079 x86 instructions
95.1% dynamic instructions
18➙32➙8➙2
Error: 19.7%
Compression jpeg
1,257 x86 instructions
56.3% dynamic instructions
64➙16➙8➙64
Error: 8.4%
Machine Learning kmeans
26 x86 instructions
29.7% dynamic instructions
6➙8➙4➙1
Error: 7.3%
Image Processing sobel
88 x86 instructions
57.1% dynamic instructions
9➙8➙1
Error: 5.2%
Financial blackscholes
309 x86 instructions
97.2% dynamic instructions
6➙8➙8➙1
Error: 10.2%
30

## Slide 31: Speedup with A-NPU over 8-bit D-NPU
Chart: Speedup over 8-bit D-NPU
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
Speedup | 2.5 | 1.8 | 2.4 | 3.9 | 15.2 | 2.4 | 2.7 | 3.3
15.2×
3.3× geometric mean speedup
Ranges from 1.8× to 15.2×

## Slide 32: Energy savings with A-NPU over 8-bit D-NPU
Chart: Energy savings over 8-bit D-NPU
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
Energy Saving | 9.5 | 3.7 | 4.5 | 28.2 | 82.2 | 8.5 | 11.8 | 12.1
82.2×
28.2×
12.1× geometric mean speedup
Ranges from 3.7× to 82.2×

## Slide 33: Dynamic Instruction Reduction
Chart: Percentage of Instructions Subsumed
Chart: Percentage of Instructions Subsumed
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
 | 0.972 | 0.674 | 0.959 | 0.951 | 0.563 | 0.297 | 0.571 | 0.66423
66.4%

## Slide 34: Speedup with A-NPU acceleration
Chart: Sppedup over All-CPU Execution
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
speedup | 24.5 | 1.3 | 10.9 | 6.2 | 1.8 | 0.8 | 3.1 | 3.7
Chart: Sppedup over All-CPU Execution
3.7× geometric mean speedup
Ranges from 0.8× to 24.5×
24.5×

## Slide 35: Energy savings with A-NPU acceleration
Chart: Energy Savings / All-CPU Execution
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
speedup | 51.2 | 1.7 | 30 | 17.8 | 2.3 | 1.3 | 2.8 | 6.3
6.3× geometric mean energy reduction
All benchmarks benefit
51.2×
30.0×
17.8×

## Slide 36: Speedup with A-NPU over 8-bit D-NPU
Chart: Speedup over 8-bit D-NPU
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
Speedup | 2.5 | 1.8 | 2.4 | 3.9 | 15.2 | 2.4 | 2.7 | 3.3
15.2×
3.3× geometric mean speedup
Ranges from 1.8× to 15.2×
Notes: Lets do a more head to head comparison between digital and analog NPUs.
Write the jpeg case
The larger the network, the higher the degree of parallelsim, the higher the benefits with analog NPU.

## Slide 37: Energy savings with A-NPU acceleration
Chart: Energy Savings / All-CPU Execution
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
speedup | 51.2 | 1.7 | 30 | 17.8 | 2.3 | 1.3 | 2.8 | 6.3
6.3× geometric mean energy reduction
All benchmarks benefit
51.2×
30.0×
17.8×

## Slide 38: Energy savings with A-NPU over 8-bit D-NPU
Chart: Energy savings over 8-bit D-NPU
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
Energy Saving | 9.5 | 3.7 | 4.5 | 28.2 | 82.2 | 8.5 | 11.8 | 12.1
82.2×
28.2×
12.1× geometric mean speedup
Ranges from 3.7× to 82.2×
Notes: Again, remember that we ate doing addition and multiplication with Ohm and Krishaf law

## Slide 39: Speedup with A-NPU acceleration
Chart: Sppedup over All-CPU Execution
| blackscholes | fft | inversek2j | jmeint | jpeg | kmeans | sobel | geomean
speedup | 24.5 | 1.3 | 10.9 | 6.2 | 1.8 | 0.8 | 3.1 | 3.7
Chart: Sppedup over All-CPU Execution
3.7× geometric mean speedup
Ranges from 0.8× to 24.5×
24.5×

## Slide 40: Neural algorithmic transformation
Analog Neural Network
Core
Analog Neural Processing Unit
A-NPU
Analog Neural Network
Esmaeilzadeh, Sampson, Ceze, Burger, “Neural Acceleration for General-Purpose Approximate Programs,” MICRO 2012.
Notes: The recent work on Neural Processing Units provides a path forward.
In MICRO 2012, they provide an algorithmic transformation that converts approximble regions of code written in conventional programming languages to neural networks.
Then, they utilize a very efficient digital accelerators to execute the neural network.
In the MICRO 2012 paper, they used a digital neural accelerator and here we use analog circuits to execute the neural network.
However, we had to redesign the whole algorithmic transformation to accommodate for the limitations of the analog circuits.