## Slide 1
Neural Acceleration for GPU Throughput Processors
Alternative Computing Technologies (ACT) Lab
Georgia Institute of Technology
Amir Yazdanbakhsh
Jongse Park
Hardik Sharma
Hadi Esmaeilzadeh
Pejman Lotfi-Kamran*
*The Institute for Research in Fundamental Sciences
NGPU
Neurally Accelerated GPU
Notes: Thank you Babak for the introduction.
Aloha everyone 
Today I am going to explain how to design a scalable low-overhead neurally accelerated GPU or as how we name it NGPU.
This is a collaborative work between Georgia Institute of Technology, where I am working under the supervision of Prof. Hadi Esmaeilzadeh, and the Institute for Research in Fundamental Sciences in Iran.

## Slide 2: Approximate computing Embracing imprecision
Relax the abstraction of “near perfect” accuracy in
Accept imprecision to improve
performance
energy dissipation
resource utilization efficiency
Data Processing
Storage
Communication
Notes: Approximate computing provides an opportunity to relax the abstraction of near perfect accuracy in
Data Processing
Storage
Communication
So you can get significant benefits in terms of performance, energy efficiency and hardware cost
In this work we focus on approximation in data processing within GPUs

## Slide 3: Opportunity
Many GPU applications are amenable to approximation
Augmented Reality
Computer Vision
Robotics
Machine Learning
Sensor Processing
Multimedia
Notes: Many GPU applications from variety of domains such as augmented reality, computer vision, sensor processing and machine learning
are amenable to approximation.
So if I introduce a little bit of error in their computation, it’s not gonna be end of the world.

## Slide 4: Opportunity
Chart: 
| binarization | blackscholes | convolution | inversek2j | jmeint | laplacian | meanfilter | newton-raph | sobel | srad | geomean
approximable | 0.71 | 0.62 | 0.29 | 0.04 | 0.42 | 0.63 | 0.38 | 0.03 | 0.64 | 0.61 | 0.44
non-approximable | 0.29 | 0.38 | 0.71 | 0.96 | 0.58 | 0.37 | 0.62 | 0.97 | 0.36 | 0.39 | 0.56
More than 55% of application runtime and energy is in neurally approximable regions
Runtime
Approximable
Non-Approximable
Notes: In fact, as you can see here and we have observed in our study on average more than 55% of application runtime and energy is spent on neurally approximable regions.
In some applications such as inverke2j, this number increases to more than 90%.
There is clearly an opportunity here that motivates us to explore the design of neural accelerators for GPUs.
Let me explain what is neurally approximable region in GPUs.

## Slide 5: Neural Transformation for GPUs
Neural Network
Neural Network
Notes: We ask the programmer to write a program in CUDA.
The programmer annotates a region of code as neurally approximable
Which means If I introduce a little bit of error it’s not going to be terrible to the user.
From now on, everything is automatic and the programmer does not have to be involved at all.
I am going to put two probes in the input and output of that region.
Then, I’m going to run the program with a lot of test inputs and monitor the inputs and outputs to that particular region.
Now I start training a neural network with the captured input-output pairs.
The goal here is to find a neural network that mimics the annotated region of code.
After the neural network model reaches a certain level of accuracy, I can replace this code with that neural network model.

## Slide 6: Challenges
Many Core
Notes: Let’s see what are the challenges here.
GPUs have many many SIMD lanes.
And we want to augment each of these cores with a neural accelerator. The reason is that we do not want to hurt the SIMD execution model in GPUs.
This means that we need to design a scalable low-overhead hardware that can be embedded into each of the core in GPU.

## Slide 7: Challenges
Many Core
Simple
In Order
Data-level
Parallelism
Notes: And also remember that each core is just a simple in-order core and we don’t want to add too much complexity around each of these cores.
The cores are simple and we want to keep them simple.

## Slide 8: Challenges
Many Core
Simple
In Order
Data-level
Parallelism
Notes: Finally, GPU already exploits large-scale data-level parallelism so it is not clear whether or not accelerating each thread beyond a certain point lead to significant benefits.
Because there are other bottlenecks in the system such as bandwidth.

## Slide 9: Challenges
Augmenting the CPU based neural processing units to each SIMD lane imposes 31.2% area overhead
Many Core
Simple
In Order
Data-level
Parallelism
Notes: In fact, if we take our CPU based neural processing unit and glue it to each core, you will see a significant area-overhead (almost 31%).
Which I don’t think it is a reasonable approach.

## Slide 10
NGPU Neurally-Accelerated GPU Architecture
Notes: Now let’s take a look at the microarchitecuture of NGPU.
So in NGPU, instead of adding bulky cpu-based neural processing unit to each core,
We have just modified the part of SIMD lanes that performs arithmetic computations in GPUs and make them capable of efficient execution of neural networks.
We have kept the front-end and back-end of GPUs almost intact.

## Slide 11: Neuronal Network Operations
Chart: 
Notes: Before diving into the details of microarchitecure,
let me say what we want to do with a neural network.
The computation of a neural network has very simple operations multiply and add and a sigmoid operation at the end.

## Slide 12: NGPU Neurally-Accelerated GPU Architecture
Notes: Here you can see the microarchitecture of NGPU.
Let me touch upon some of the consideration that we had in our design to make the architecture simple.

## Slide 13: NGPU Neurally-Accelerated GPU Architecture
NGPU reuses the existing ALU in each SIMD lane
Notes: We reuse the existing ALU units in each SIMD lane because they are already capable of execution multiply accumulate.
and we added a Sigmoid unit which is synthesized as a ROM.

## Slide 14: NGPU Neurally-Accelerated GPU Architecture
Weight FIFO is shared among all the SIMD lanes
Notes: We utilized the same SIMD execution model in NGPU.
In this model, SIMD lanes execute same code.
So we can actually share the weight buffer across all the threads which actually reduces the area overhead.
But we have to add an input/output buffer which holds the inputs and outputs of the neural network
and an accumulate register to each SIMD lane.

## Slide 15: NGPU Neurally-Accelerated GPU Architecture
Overall NGPU has ≤1% area overhead
Notes: With all these considerations, our design adds around 1% area overhead to the GPU

## Slide 16: NGPU Execution Model
Neural Network
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
Neurally Accelerated GPU Application
Notes: Now that we got familiar with the microarchitecture of our design.
Let’s take a look at the ngpu exeuction model.
After neural transformation, the code has two parts:
(1) one is the normal part which performs exact computation
(2) the other part which invokes the GPU to enter the neural mode.
And the activation happens through a set of ISA extensions that actually send the data to the neurally accelerated SIMD lanes and retrieves the results.

## Slide 17: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
Notes: Just explain what is here!!!

## Slide 18: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
SIMD lanes are in normal mode and performs precise computation

## Slide 19: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
SIMD lanes enter neural mode
Notes: You start sending the inputs to SIMD lanes through our ISA extensions
This also takes the SIMD lanes into the neural mode.

## Slide 20: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
SIMD starts the calculation of the neural network
Notes: Now the GPU stops issuing new instructions and
then SIMD lanes get into the neural mode and
start calculating the neural network.

## Slide 21: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The neurally accelerated SIMD lanes autonomously calculate the neural outputs in lock-step
Notes: The neurally accelerated SIMD lanes autonomously calculate the neural outputs in lock-step
For example here you can see that weight zero is multiplied by the corresponding input in each SIMD lane

## Slide 22: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The accelerated SIMD lanes autonomously calculate the neural outputs in lock-step

## Slide 23: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The accelerated SIMD lanes autonomously calculate the neural outputs in lock-step

## Slide 24: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The accelerated SIMD lanes autonomously calculate the neural outputs in lock-step

## Slide 25: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The accelerated SIMD lanes autonomously calculate the neural outputs in lock-step

## Slide 26: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The accelerated SIMD lanes autonomously calculate the neural outputs in lock-step

## Slide 27: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The accelerated SIMD lanes autonomously calculate the neural outputs in lock-step

## Slide 28: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The accelerated SIMD lanes autonomously calculate the neural outputs in lock-step

## Slide 29: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
The accelerated SIMD lanes autonomously calculate the neural outputs in lock-step

## Slide 30: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
SIMD lanes exit neural mode
Notes: At this point that the output data is ready
we can unblock the issuing new instructions and retrieve the data from the output FIFOs in SIMD lanes.

## Slide 31: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
( in0, in0, …, in0)
( in1, in1, …, in1)
w0 × ( in0, in0, …, in0)
+ w2 × ( in1, in1, …, in1)
sigmoid
w1 × ( in0, in0, …, in0)
+ w3 × ( in1, in1, …, in1)
sigmoid
w4 × ( n0, n0, …, n0)
+ w5 × ( n1, n1, …, n1)
sigmoid
( out0, out0, …, out0)
SIMD lanes are in normal mode
Notes: And now we are back into the normal mode and SIMD lanes continue the execution in the nornal mode.

## Slide 32: Experimental Setup
Power Model
Technology Node 40 nm
GPUWattch
McPAT and CACTI, Verilog
GPU Simulator
GPGPUSim Cycle-Level Simulator
Fermi-based GTX 480, Shader Core Frequency 1.4 GHz
NVCC Compiler –O3
Machine Learning, Finance, Vision 3D Gaming, Medical Imaging Numerical Analysis, Image Processing
Notes: We evaluated NGPU with a diverse set of applications such as machine learning, finance, vision, medical imaging
For the simulation, we use the GPGPUSim cycle-level simulator. We modified the GPGPUSim to include the NGPU ISA and the extra microarchitectural components necessary for the integration of neural accelerators within GPUs.
We use GPGPUSim’s default configuration that closely model GTX 480 chipset which is based on the Fermi microarchitecture.
Having said that, let’s take a look at some of the results.

## Slide 33: NGPU Speedup
Speedup
Most applications see speedup with NGPU
Chart: 
| binarization | blackscholes | convolution | inversek2j | jmeint | laplacian | meanfilter | newton-raph | sobel | srad | geomean
 | 1.39 | 1.02 | 2.96 | 9.81 | 1.92 | 1.49 | 2.21 | 14.29 | 1.47 | 1.05 | 2.37
2.4×
9.8×
14.3×
×
×
×
×
×
Notes: Most of the applications see speedup with NGPU and on average, NGPU delivers 2.4 speedup.
Some application such as inversek2j and newton-raph see significant speedup with NGPU and these are the applications that large region of code is replaced with a neural network.

## Slide 34: NGPU Speedup
Speedup
The speedup for bandwidth-sensitive applications is limited
Chart: 
| binarization | blackscholes | convolution | inversek2j | jmeint | laplacian | meanfilter | newton-raph | sobel | srad | geomean
 | 1.39 | 1.02 | 2.96 | 9.81 | 1.92 | 1.49 | 2.21 | 14.29 | 1.47 | 1.05 | 2.37
2.4×
9.8×
14.3×
×
×
×
×
×
Notes: There are two outliers here highlighted with red circles.
Blackscholes and srad.
These applications belong to the category of bandwidth-sensitive applications.
When we accelerate these codes we put more pressure on the bandwidth.
So we see small speedup in these applications.

## Slide 35: NGPU Speedup with 2x Bandwidth
Chart: 
| binarization | blackscholes | convolution | inversek2j | jmeint | laplacian | meanfilter | newton-raph | sobel | srad | geomean
 | 1.39 | 1.02 | 2.96 | 9.81 | 1.92 | 1.49 | 2.21 | 14.29 | 1.47 | 1.05 | 2.37
Speedup
Bandwidth-sensitive applications see speedup with 2x bandwidth
3.0×
14.6×
15.3×
×
×
×
×
×
Notes: However, if we increase the bandwidth by the factor of 2 which can be obtained with 3d stacking and compression, the bandwidth sensitive applications also see speedup.
Let’s see how NGPU improves the energy efficiency.

## Slide 36
Chart: 
| binarization | blackscholes | convolution | inversek2j | jmeint | laplacian | meanfilter | newton-raph | sobel | srad | geomean
 | 1.99 | 2.12 | 3.02 | 18.93 | 1.3 | 1.56 | 1.63 | 14.7 | 1.6 | 1.41 | 2.77
18.9×
14.8×
Energy Reduction
NGPU eliminates the von Neumann overhead which results in energy reduction
2.8×
NGPU Energy Savings with Baseline Bandwidth
×
×
×
×
×
Notes: Here we shows the whole application energy reduction with the baseline bandwidth.
On average we see 2.8x energy reduction by using NGPU.
This result is due to the fact the NPGU eliminates the von Neuman overhead such as fetching and decoding the instructions
Moreover, we perform computations locally inside each SIMD lane and we don’t access the register file after each operation.

## Slide 37
Chart: 
| binarization | blackscholes | convolution | inversek2j | jmeint | laplacian | meanfilter | newton-raph | sobel | srad | geomean
 | 1.99 | 2.12 | 3.02 | 18.93 | 1.3 | 1.56 | 1.63 | 14.7 | 1.6 | 1.41 | 2.77
18.9×
14.8×
Energy Reduction
Even bandwidth-sensitive applications see energy saving
2.8×
×
×
×
×
×
NGPU Energy Savings with Baseline Bandwidth
Notes: These are all help to save power that translate to energy saving even though in bandwidth-sensitive applications the speedup is marginal.

## Slide 38: Application Quality Loss
Chart: 
| binarization | blackscholes | convolution | inversek2j | jmeint | laplacian | meanfilter | newton-raph | sobel | srad | average
 | 0.0823 | 0.0435 | 0.0525 | 0.0873 | 0.097 | 0.0601 | 0.0706 | 0.0308 | 0.0545 | 0.0743 | 0.06529
Quality loss is below 10% in all cases
Quality Loss
Notes: But this is not the end of story, we are paying something for these benefits.
And it is the loss in the output quality.
Here, I show you the output quality loss across all the benechmarks.
All the quality losses are measured based on the application-specific quality metric.
We have introduced a quality control mechanism that helps us to keep the quality loss in all application below 10%.
Our quality control mechanism for NGPU is explained in details in the paper and I encourage you all to read the paper for more details about it.

## Slide 39: NGPU is a Fair Bargain
Quality ≥ 97.5%
1.9×
Speedup
2.1×
Energy Reduction
Quality ≥ 90.0%
2.4×
Speedup
2.8×
Energy Reduction
Area Overhead ≤ 1.0%
Overhead
Benefits
Notes: If we look at what we have done here.
With around 1% area overhead
And 2.5% loss in the output quality, NGPU delivers around 2.0x in speedup and energy reduction.
And if we allow 10% loss in the quality, the benefits increase and NGPU provides 2.4x speedup and 2.8x energy reduction.
So these results suggest that NGPU may be a fair bargain.
******* WAIT A LITTLE ********
When we published the neural accelerator paper for CPUs, many people asked us why not using GPUs.
And there you go.
In this work, we introduced NGPU, a scalable neurally accelerated GPU that can even accelerate GPU accelerators.
And by that I’d be happy to take questions

## Slide 40: Backup Slides

## Slide 41: Overheads
GNPU Components | Configuration
Weight FIFO | 2 KB / SM
Input FIFO | 256 bytes / SIMD Lane
Output FIFO | 256 bytes / SIMD Lane
Sigmoid LUT | 2048 x 32-bit / SIMD Lane

## Slide 42: Benchmarks
Image Processing binarization
27 PTX instructions
3➙4➙2➙1
Error: 8.23%
Finance blackscholes
96 PTX instructions
6➙8➙1
Error: 4.35%
Machine Learning convolution
886 PTX instructions
17➙2➙1
Error: 5.25%
Robotics inversek2j
132 PTX instructions
2➙16➙3
Error: 8.73%
3D Gaming jmeint
2,250PTX instructions
18➙8➙2
Error: 9.70%
Image Processing laplacian
51 PTX instructions
9➙2➙1
Error: 6.01%
Machine Vision meanfilter
35 PTX instructions
7➙4➙1
Error: 7.06%
Numerical Analysis newton-raph
44 PTX instructions
5➙2➙1
Error: 3.08%
Image Processing sobel
86 PTX instructions
9➙4➙1
Error: 5.45%
Medical Imaging srad
110 PTX instructions
5➙4➙1
Error: 7.43%

## Slide 43: Motivation Runtime Breakdown
Runtime
Approximable
Non-Approximable

## Slide 44: Motivation Energy Breakdown
Energy
Approximable
Non-Approximable

## Slide 45: Motivation Software Implementation
Slowdown

## Slide 46: Adding a third dimension Embracing Error
Error
IoT
Mobile
Desktop
Data center

## Slide 47: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
SIMD lanes are in normal mode
The SM performs precise computation

## Slide 48: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
SIMD lanes enter neural mode
The SM sends the inputs to each of the SIMD lanes

## Slide 49: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
SIMD lanes autonomously
calculate the neural outputs
The SM waits for the neurally enhanced SIMD lanes to finish calculating the neural outputs

## Slide 50: NGPU Execution Model
ld.global %r0, [addr0];
ld.global %r1, [addr1];
send.n_data %r0;
send.n_data %r1;
recv.n_data %r2;
st.global [addr2], %r2;
SIMD lanes autonomously
calculate the neural outputs
The SM waits for the neurally enhanced SIMD lanes to finish calculating the neural outputs

## Slide 51: NGPU is a Fair Bargain
2.4×
Speedup
2.8×
Energy Reduction
≥90.0%
Quality
A scalable neurally accelerated architecture for GPUs with ≤ 1.0% area overhead
1.9×
Speedup
2.1×
Energy Reduction
≥97.5%
Quality
Notes: Happy to take questions

## Slide 52
Error
Navigating a three dimensional space
IoT
Mobile
Desktop
Data center

## Slide 53: Neural Accelerator Design Alternatives
CPU
NPU
CPU
GPU
FPGA
Digital ASIC
FPAA
Analog ASIC
(Speed: 2.3×↑, Energy: 3.0×↓, Quality: 10%↓)
(Speed: 3.7×↑, Energy: 6.3×↓, Quality: 10%↓)
(Speed: 1.8×↑, Energy: 1.7×↓, Quality: 10%↓)
Notes: The actual reason that I come up with the idea was to use analog circuits to do general-purpose computing without changing the programing model.
I thought about this algorithmic transformation.
Now, what I am aspiring toward is using biological nervous tissues to do parts of the programs written in C or Java.

## Slide 54
NGPU Neurally-Accelerated GPU Architecture
Notes: So in NGPU, instead of adding bulky cpu-based npu to each core, we slightly modify the SIMD lanes in the GPUs and make them capable of efficient execution of neural networks.

## Slide 55: Neural Networks and Intermediate Representation
Neural Representation
Code1
Code2
Code3
Code4
Code5
Code6
…
Source Codes
Common Intermediate Representation
Acceleration
+
×
Chart: 
Neurally Accelerated GPU
Notes: Our goal here is to take different regions of code from diverse sets of applications and execute them using a neural model.
Our studies show that different regions require different topologies of the neural network.
Therefore, it is critical that our neurally accelerated hardware be reconfigurable, dynamically adapting to many different regions of code.
To this end we are taking different parts from various GPU applications and converting them to an intermediate neural representation which has simple operations
Addition
Multiplication
Sigmoid unit
Now let’s take a look at what are the challenges to design a neurally accelerated GPU.

## Slide 56: Data Growth vs. Performance
Performance growth trends: Esmaeilzadeh et al, “Dark Silicon and the End of Multicore Scaling,” ISCA 2011.
Data growth trends: IDC's Digital Universe Study, December 2012.

## Slide 57: NGPU Neurally-Accelerated GPU Architecture
Controller handles the neural execution of all the SIMD lanes

## Slide 58
≤1%
Area Overhead
2.4×
Speedup
2.8×
Energy Reduction
≥90%
Quality
NGPU