## Slide 1: Bit Fusion
Bit-Level Dynamically Composable Architecture for Deep Neural Networks
Hardik Sharma
Jongse Park
Naveen Suda†
Liangzhen Lai†
Benson Chau
Vikas Chandra†
Hadi Esmaeilzadeh‡
Alternative Computing Technologies (ACT) Lab
†Arm, Inc.
Georgia Institute of Technology
‡University of California, San Diego
Notes: Hi. I am Hardik Sharma and today I would like to present our work BitFusion, a bit-level dynamically composable architecture for deep neural networks (DNNs)

## Slide 2: DNNs Tolerate Low-Bitwidth Operations
>99.4% Multiply-Adds require less than 8-bits
Notes: Very recent work in machine learning has shown that you can reduce the bitwidth for DNN operations, without losing accuracy.
However, to avoid loss in accuracy, the bitwidth varies for different DNNs and within layers of a DNN, and we show that trend here.
The x-axis shows 8 different low-bitwidth benchmark DNNs, including RNNs and LSTMs. The different colors in the y-axis show the different bitwidths required by these DNNs to achieve the same accuracy as the original floating-point model.
We can see here that most of the multiply-adds, more than 99.4%, require less than 8-bit precision. BitFusion aims to leverage this opportunity of low bitwidth for DNN operations to improve performance and efficiency.
+40
00:55

## Slide 3
Bitwidth Flexibility is Necessary for Accuracy
A fixed-bitwidth accelerator would either achieve limited benefits (8-bit), or compromise on accuracy (<8-bit)
Notes: Here, we take a look at two example DNNs proposed by recent literature.
The first example, is a low-bitwidth AlexNet network trained on the IMAGENET dataset recently proposed by WRPN requires both 8-bit and 4-bit operands
On the other hand, LeNet trained on the MNIST dataset uses 2-bit operands
Therefore, a fixed-bitwidth accelerator would either achieve limited benefits to account for the highest possible bitwidths requirements, which is 8-bit in this case, or compromise accuracy for improving performance or energy efficiency
To this end, BitFusion is a bit-flexible architecture that can matches the bitwidths require by DNN layers to achieve performance and energy benefits without sacrificing accuracy
+40
01:35

## Slide 4
Our Approach: Bit-level Composability
BitBricks (BBs) are bit-level composable compute units
Notes: BitFusion defines a new dimension of bit-level composability in the design of DNN accelerators
To enable composability at the bit level, the physical element for computations in our design is a bitbrick that can perform 2-bit by 2-bit multiplications
A Fusion unit consists of 16 of these BitBricks along with glue logic that allows the bitbricks to compose and decompose dynamically at runtime to match the bitwidth required by individual DNN layers
Let's see how that works
Empirically 1 bit was not effective! We needed both signed and unsigned!
02:50
repeated composability

## Slide 5
Compute units (BitBricks) logically fuse at runtime to form Fused-PEs (F-PEs) that dynamically match bit-width of the DNN layers
Notes: Figure a shows a physical grouping of 16 bitbricks, which we call a fusion unit.
Within a fusion unit, bitbricks can logically compose to form Fused Processing Engines (F-PEs), match the bitwidth of individual DNN layers
If a DNN layer requires 2-bit precision, as shown in figure b, the bitbricks work individually to yield the highest parallelism
To support 8-bit inputs and 2-bit weights, as shown in figure c, four of the bitbricks can compose to match this requirement.
Which means, the bitwidths of inputs and weights are not constrained to be symmetric
If a DNN requires even more bitwidth, all the bitbricks compose to perform a single operation
I would like to point out here that the design of a fusion unit is completely combinational and can serve as a replacement for the multipliers in conventional multipliers in even existing processors
+1:15
03:25

## Slide 6
Config #1 : Binary/Ternary Mode
Each BitBrick performs a binary/ternary multiplication
16x parallelism
Notes: Now, let’s take a deeper look at how the Fusion unit enables bit-level composability
The simplest case is when we need 2-bit precision, each bitbrick works independently to generate a single partial result.
All the partial results are then added together to generate a single result
+00:20

## Slide 7
Config #2: 4-bit Mode
Four BitBricks fuse to form a Fused-PE (F-PE)
4x Parallelism
Notes: The second configuration requires 4-bit by 4-bit computations
To do this, we first break down the original 4-bit multiplication is broken into 4 partial products.
These partial products are then mapped to bitbricks in a fused-PE, and hence, each fusion unit performs 4 operations in parallel
5:10

## Slide 8
Config #3 : 8-bit, 4-bit (Mixed-Mode)
Eight BitBricks fuse to form a Fused-PE (F-PE)
2x Parallelism
Notes: To support 8-bit by 4-bit mode, 8 bitbricks fuse together to form a Fused Processing Engines (F-PEs) that can perform computations with the required bitwidths.
Each Fused-PE performs a single multiply operation, which yields a 2x parallelism
We call this approach of spatially composing bitbricks spatial fusion

## Slide 9
Spatial Fusion vs. Temporal Design
Temporal Design (Bit Serial): Combine results over time
Spatial Fusion (Bit Parallel): Combine results over space
Notes: As an alternative to spatial fusion approach explored in Bit Fusion, prior work has explored a temporal design that uses bit-serial computation
The figure on the left shows temporal design.
In contrast, spatial fusion combines the results over space, by adding together partial results generated by bitbricks

## Slide 10
Spatial Fusion Surpasses Temporal Design
Area (um^2) | BitBricks | Shift-Add | Register | Total Area
Temporal | 463 | 2989 | 1454 | 4905
Fusion Unit | 369 | 934 | 91 | 1394
Power (nW) | BitBricks | Shift-Add | Register | Total Power
Temporal | 60 | 550 | 1103 | 1712
Fusion Unit | 46 | 424 | 69 | 538
Synthesized using a commercial 45 nm technology |  |  |  | 
3.5x lower area
3.2x lower power
Notes: For the same throughput, a temporal design requires significantly higher area and power compared to fusion unit
As we can see, the area and power for bitbricks, which are the multipliers in the design, are almost the same
Most of the benefits come from sharing the shift-add unit and the register across bitbricks

## Slide 11
Bit Fusion Systolic Array Architecture
Notes: Bit-level composability is orthogonal to organization of resources
In this work, we evaluate BitFusion in the context of a 2D systolic array architecture
+00:20

## Slide 12: Programmability: BitFusion ISA
Requirements
Amortize cost of bit-level fusion
Enable flexible Data-Path
Concise
Notes: Now that we have designed this bit-level composable architecture, the next challenge is to make it programmable to support a wide range of DNNs and their bitwidth requirements.
To this end, we set aside three requirements for the ISA
The first requirement is to amortize the cost of bit-level fusion across the millions of operations required by DNNs
Next, we want to express the computations in a DNN layer with the fewest possible instructions
Finally, we need to adapt the data-path according to the bitwidth requirements.

## Slide 13: ISA: Amortize the Cost of Bit-Level Fusion
Use a block-structured ISA for groups of operations (layers)
Notes: The computations in a DNN are divided into groups, called layers.
To avoid the overhead of fine-grained control over the bitwidths at the scale of a Deep Neural Network, we propose a block-structured ISA.
This block structured ISA that uses instruction blocks to express bitwidth requirements at a per-layer granularity.

## Slide 14: ISA: Concise Expression for DNNs
Use loop instructions as DNNs consist of large number of repeated operations
Fully-Connected Layer
Notes: DNN layers consists of simple mathematical operations that are repeated over millions of times.
To this end, the ISA uses loop instructions to concisely express the computations repeated in a DNN layer and minimize the overhead of instruction fetch and decode.

## Slide 15: ISA: Concise Expression for DNNs
DNNs have regular memory access pattern
Use loop indices to generate memory accesses
Fully-Connected Layer
Notes: Finally, DNNs have highly regular memory access patterns.
These memory access can be concisely expressed as a linear function of the loop indices.

## Slide 16: ISA: Flexible Storage
ISA changes the semantics of off-chip and on-chip memory accesses according to bitwidth of operands
Notes: Finally, the ISA changes the semantics of the memory accesses according to the bitwidth requirement

## Slide 17: ISA: Flexible Storage (Software View)
Software views the buffers as having a flexible aspect ratio
Notes: The software then views the on-chip buffers as memory units with a flexible aspect ratio
For more details on the bitfusion architecture and its ISA I refer you to the paper

## Slide 18: Benchmarked Platforms
Notes: We compare BitFusion to four execution platforms.
The first two are the Nvidia Tegra TX2 GPU and the Titan X GPU based on the pascal architecture
We further compare BitFusion to two state of the art accelerators – Stripes and Eyeriss

## Slide 19: Benchmarked DNN Models
Notes: We use a wide range of DNNs to evaluate the benefits from BitFusion.
These are DNNs proposed by recent literature that use propose low-bitwidth DNNs, including vanilla RNNs and even LSTMs
The model sizes vary between 0.5 to 116 MB, while the computational complexity varies between 13 million to 4 billion operations

## Slide 20: Comparison with Eyeriss
3.9× speedup and 5.1× energy reduction over Eyeriss
Notes: We use the open-source Tetris simulator to estimate the energy consumption and performance for eyeriss.
While Eyeriss is an optimized dataflow architecture, it uses fixed 16-bit computational units.
BitFusion, on the other hand, matches the bitwidth requirements of the DNN at finest granularity, at the bit-level.

## Slide 21: Comparison with Stripes
2.6× speedup and 3.9× energy reduction over Stripes
Notes: Next, we compare against Stripes, a bit-serial architecture that uses a fixed 16bit weights and variable bitwidth inputs.
BitFusion on the other hand enables variable bitwidths for both inputs and weights.

## Slide 22: Comparison with GPUs
Bit Fusion provides almost the same performance as Titan Xp (250 W) with only 895 mW
Notes: BitFusion is 16 times faster than TX2 but performs18% slower than Titan Xp
While Titan Xp has a 250 Watt TDP, BitFusion uses just 895 milliwatts on average.
The benefits come primarily come from bit-level fusion capabilities offered by BitFusion.

## Slide 23: Conclusion
Emerging research shows we can reduce bitwidths for DNNs without losing accuracy
Bit Fusion defines a new dimension of bit-level dynamic composability to leverage this opportunity
BitFusion ISA exposes this capability to software stack
Notes: Utilizing algorithmic innovations to rethink the hardware allows us to optimize computations, on-chip storage, and off-chip accesses at the finest granularity possible, bit-level
By leveraging this insight, BitFusion defines a new dimension in design of DNN accelerators, which is bit-level composability
We believe, that such an microrarchitectural approach can be extended to other domains such as robotics, IoT, and data analytics

## Slide 24
Notes: I would love to take questions

## Slide 25: DRAM Accesses Bottleneck Energy Benefits
DRAM accesses consume ~70% of total Energy
Notes: While Eyeriss consumes 37% energy for off-chip acesses

## Slide 26
> 95% of DNN weights require less than 8-bits
Tolerance to low bitwidth in DNN weights

## Slide 27: DNNs Tolerate Low-Bitwidth Operations
>99.4% Multiply-Adds require less than 8-bits
Notes: Past work in machine learning has shown that you can reduce the bitwidth for DNN operations, without losing accuracy.
However, to avoid loss in accuracy, the bitwidth varies for different DNNs and within layers of a DNN.
Here, we look at 8 different low-bitwidth benchmark DNNs, including RNNs and LSTMs, that were proposed by recent machine learning literature.
2 years of research to get to the levels of accuracy.
The table on the left shows that across eight DNNs the dominant operation is the multiply-add operation
The barchart on the right shows the 8 different DNN benchmarks on the x-axis and the breakdown of the bitwidths required for the multiply-adds in the y-axis.
We can see here that most of the multiply-adds, more than 99.4%, require less than 8-bit precision. BitFusion aims to leverage this opportunity of low bitwidth for DNN operations to improve performance and efficiency
+40
00:55

## Slide 28
Opportunity for performance/energy benefits
Quadratic improvement in Speedup, Linear in Energy

## Slide 29
BitFusion Systolic Array
BitFusion offers 512 Fusion Units and 8192 BitBricks
same area budget (5.87 mm2) as Eyeriss (168 PEs)
Notes: 1 Op/cycle/FusionUnit 512 Ops/cycle
16 Op/cycle/FusionUnit 8192 Ops/cycle

## Slide 30: Loop Blocking
Loop blocking to maximize on-chip data reuse

## Slide 31: Loop Reordering
Loop reordering allows switching between Input stationary and output stationary, depending on DNN layer